## Slide 1: Multiphysics Simulation of Battery Cells and Packs for Electric Vehicles
Joseph M. Barakat, Mark S. Oliver & Matthew J. Hancock
Veryst Engineering LLC, Needham, MA, USA
 jbarakat@veryst.com  www.veryst.com
COMSOL Conference 2024, Boston, MA, USA

## Slide 2: Simulation for EV Battery Development
New battery technologies must satisfy certain targets prior to commercialization:
  Safety
  Cost
  Performance
Multiphysics simulation can help solve various challenges to meet these targets:
  Electrochemical
  Thermal
  Mechanical

## Slide 3: Increasing Battery System Performance
Cell
Module
Pack
Vehicle
Innovation Drivers:
  Lower Cost
  Lower Weight
  Simpler Manufacturing
  Higher Energy Density
  Smaller Form Factor
Cell-to-Module
Mobile Power
Automotive
Rail
Aircraft
Cell-to-Pack
Cell-to-Chassis
Cell-to-Vehicle

## Slide 4: Multiphysics Challenges in Battery Systems
 | Electro- chemical | Thermal | Mechanical
Cell Level | Voltage losses Capacity fade and aging Lifetime performance | Heat dissipation | Volume expansion Internal stresses Delamination and cracking
Module Level | Cell-to-cell state of charge variability Voltage imbalances | Cell-to-cell temperature uniformity Cooling efficiency | Compact form factor Thermal stresses Aging and degradation
Pack Level | State of charge estimation Over-discharge | Module-to-module temperature uniformity Safety and thermal management | Lightweighting Structural adhesives Structural durability
Li+

## Slide 5: COMSOL Multiphysics® Simulations
I think
Li+
Lifetime Performance
Thermal Management
Structural Durability

## Slide 6: COMSOL Multiphysics® Simulations
Li+
Lifetime Performance
Thermal Management
Structural Durability

## Slide 7: Simulating the Hybrid Pulse Power Characterization (HPPC) Test
HPPC test = sequence of charge + discharge pulses to measure battery’s life performance.
Veryst simulated cell voltage response over 13 hours (simulation time << experimental time).
4
0
V
Li+
Voltage

## Slide 8: Direct Calculation of Voltage Losses
Voltage loss is attributed to
  ohmic resistances
  activation of electrode kinetics
  concentration-driven ion transport
Each loss term can be evaluated as COMSOL Variables, allowing direct measure of battery performance.
Li+

## Slide 9: Results: Charge vs. Discharge Response
Key factors that affect performance are electrode material selection, electrode microstructure, and electrolyte conductivity and stability.
Li+
Discharge
Charge
Capacity Increment
0.15
-0.25
0
0
100
200
Total
Ohmic
Activation
Concentration
Voltage (V)
Time (s)
45%
50%
5%
2%
43%
55%
Discharge
Charge
Ohmic
Activation
Concentration
Activation polarization is the dominant source of loss.

## Slide 10: COMSOL Multiphysics® Simulations
Li+
Lifetime Performance
Thermal Management
Structural Durability

## Slide 11: Simulating a Liquid-Cooled Battery Pack
Batteries generate significant heat, require active cooling.
Simulations can predict cooling rates to guide thermal design.
Veryst simulated temperature distribution in a liquid-cooled battery pack to determine optimal coolant flow rates.
Temperature (°C)
Cool
Fluid In
Warm
Fluid Out

## Slide 12: Results: Selecting Flow Rate to Achieve Target Battery Temperature
Line plots of maximum and minimum temperature show higher flow improves uniformity.
Flow rates > 500 ml/min required to maintain temperature < 26°C.
Key factors that influence cooling:
  Coolant selection & flow rate
  Cooling plate selection
  Thermal adhesive selection
50
40
30
20
200
400
Battery Temperature (°C)
Liquid Flow Rate (ml/min)

## Slide 13: COMSOL Multiphysics® Simulations
Li+
Lifetime Performance
Thermal Management
Structural Durability

## Slide 14: Simulating Adhesive Bonds in Packs
Cold Plate
Cell
Thermally Conductive Adhesive
Adhesives applications in batteries:
  Cell-to-cell bonding
  Cell-to-cold plate bonding
  Sealed enclosures
Greater Structural Integration
Higher Mechanical Demands on Adhesive Bonds
Greater Risk of Adhesive Failure
Veryst simulated adhesive stresses due to cyclic, torsional loading typically encountered during service.

## Slide 15: Results: Adhesive Stress Analysis
Torsional Loading
Stress analysis necessary to assess risk of fatigue debonding in cyclically loaded structures.
Cycles to Failure, N
Stress, σ
Normal Stress
Adhesive Bond Area
Stress Concentration at Corner
Time, t
Load, T
Chart: 
| 0 | 0.15707963267948966 | 0.31415926535897931 | 0.47123889803846897 | 0.62831853071795862 | 0.78539816339744828 | 0.94247779607693793 | 1.0995574287564276 | 1.2566370614359172 | 1.4137166941154069 | 1.5707963267948966 | 1.7278759594743864 | 1.8849555921538759 | 2.0420352248333655 | 2.1991148575128552 | 2.3561944901923448 | 2.5132741228718345 | 2.6703537555513241 | 2.8274333882308138 | 2.9845130209103035 | 3.1415926535897931 | 3.2986722862692828 | 3.4557519189487729 | 3.6128315516282616 | 3.7699111843077517 | 3.9269908169872414 | 4.0840704496667311 | 4.2411500823462207 | 4.3982297150257104 | 4.5553093477052 | 4.7123889803846897 | 4.8694686130641793 | 5.026548245743669 | 5.1836278784231586 | 5.3407075111026483 | 5.497787143782138 | 5.6548667764616276 | 5.8119464091411173 | 5.9690260418206069 | 6.1261056745000966 | 6.2831853071795862
 | 0 | 0.15643 | 0.30902 | 0.45399 | 0.58779 | 0.70711 | 0.80902 | 0.89101 | 0.95106 | 0.98769 | 1 | 0.98769 | 0.95106 | 0.89101 | 0.80902 | 0.70711 | 0.58779 | 0.45399 | 0.30902 | 0.15643 | 1.2251e-16 | -0.15643 | -0.30902 | -0.45399 | -0.58779 | -0.70711 | -0.80902 | -0.89101 | -0.95106 | -0.98769 | -1 | -0.98769 | -0.95106 | -0.89101 | -0.80902 | -0.70711 | -0.58779 | -0.45399 | -0.30902 | -0.15643 | -2.4503e-16

## Slide 16: Conclusions
Multiphysics simulation can help solve electrochemical, thermal, and mechanical problems for battery and automotive developers.
In this presentation, Veryst used COMSOL Multiphysics® to predict…
  internal resistances in a battery pack over range of useable capacity,
  optimal coolant flow rates to maintain desired operating temperature,
  adhesive stresses under cyclic loading that can lead to fatigue debonding.
Simulations such as these can be used to inform battery design and operating parameters to optimize performance and life behavior.